## Slide 1: PROPULSION ENGINEERING

## Slide 2: WHAT IS PROPULSION
PRO –Before OR Forward
PELLERE –To push or drive an object
PROPULSION –To push or drive an object forward

## Slide 3: AIRCRAFT ENGINE
Petrol engine : 1876 by German inventor NA OTTO.
Jet propulsion precedes piston engine hundreds of years
1903:CharlieTaylor built an inline aeroengine for the first successful flight by wright brothers at kitty hawk.

## Slide 4
Working of jet propulsion is based on newton’s third law .
When fluid is to be accelerated, force is required to produce acceleration in the fluid.
At the same time, there is an equal and opposite reaction force on the engine which is known as thrust. Working of jet propulsion is based on the reaction principle
PRINCIPLE OF JET PROPULSION

## Slide 5
CLASSIFICATION OF AIRCRAFT ENGINES
AIR BREATHING ENG
RKT ENGINES
RECIPROCATING OR PROPELLER
ENGINES
GAS TURBINE ENGINES
RAMJET ENGINES
PULSE JET ENGINES
CHEMICAL RKT ENG
COMB OF DUCTED JET ENG
AND RKT ENG
NUCLEAR RKT ENG
ELECT RKT ENG

## Slide 6: PROPULSION
Air breathing engines. Engines which use combustion gases produced by burning of fuel using atmospheric air.
Rocket engines. Engines which use jet of gas produced by the chemical reaction of the fuel and oxidizer. Each of them is carried within the system itself. No atmospheric air is used .

## Slide 7: RECIPROCATING ENGINES

## Slide 8
P
V
SUCTION
EXPANSION
EXHAUST
COMBUSTION
COMPRESSION
OTTO CYCLE

## Slide 9: TWO STROKE ENGINE

## Slide 10: FOUR STROKE ENGINE

## Slide 11: VARIOUS STAGES OF FOUR STROKE ENGINE

## Slide 12: Disadv of Const Vol Cycle
Thermal η of const vol cycle is higher
Mechanical difficulties are higher
For heat addition at const vol valves are reqd to isolate C.C
Combustion is intermittant which impairs smooth running
Difficult to design

## Slide 13: RECIPROCATING ENGINES
Used extensively as an aircraft powerplant during world WAR I &II
It drives a propeller. Propeller displaces rearwards a large amount of air, accelerating it in the process
This acceleration of the fluid produces a propulsive force which drives the aircraft

## Slide 14: RECIPROCATING ENGINES
ADVANTAGES
Fuel economy and good take off characteristics
Used in small aircraft flying at velocities less than 500 km/hr
DISADVANTAGES
Large drop in power with altitude
Need for using high octane fuel
Difficulty in cooling and lubrication
High weight to power ratio
Large frontal area

## Slide 15: AIRCRAFT PROPULSION AND ITS BACK GROUND
Gas turbine-means of producing mech power
Turbine is the most satisfying means of producing mech power. Reasons:-
  Few balancing problems
  Low oil consumption
  High reliability

## Slide 16: PRINCIPLE OF JET PROPULSION
HERO’S ENGINE
GARDEN SPRINKLER

## Slide 17: SOME INTERESTING FACTS
Jet engine-world war II
Sir Frank Whittle & Han Von Ohain
Whittle engine -1929 called power jets W.I. Flew on British Gloster g.40 on 15 may 1941.
Von Ohlin engine HES 3B IN HEINKEL HE 178.
British eng-centrifugal comp & German eng axial flow comp.

## Slide 18: BRAYTON CYCLE
P
V
comp
comb
exp
exhaust
suction

## Slide 19: SIMPLE GAS TURBINE
COMP
TUR
CC
AIR
FUEL
EXHAUST
POWER O/P
1
2
3
4

## Slide 20
TURBO-JET
TURBOPROP
TURBOFAN
TURBOSHAFT
PROPFAN
TYPES OF GAS TURBINE ENGINES

## Slide 21: OPERATING RANGE OF DIFFERENT GAS TURBINE ENGINES

## Slide 22
  IT DERIVES ITS THRUST BY HIGHLY ACCELERATING A SMALL MASS OF AIR BY EXPANDING THE GASES THROUGH THE NOZZLE
  TO OBTAIN HIGH VELOCITY THE TURBINE IS DESIGNED TO EXTRACT ONLY ENOUGH POWER FROM THE HOT GASES TO DRIVE THE COMPRESSOR AND THE ENGINE ACCESSORIES
  REST IS CONVERTED INTO KINETIC ENERGY OF THE EXHAUST.
TURBOJET ENGINE

## Slide 23: TURBOJET

## Slide 24
TURBOJET ENGINES

## Slide 26: TURBOJET ENGINE (centrifugal compressor)

## Slide 27: TURBOJET ENGINE (Axial compressor)

## Slide 28: TURBOJET ENGINE

## Slide 29: BRAYTON CYCLE
P
V
comp
comb
exp
exhaust
suction
T
S

## Slide 30: THRUST EQUATION

## Slide 31
Power unit
Thrust
Va
Thrust
Pa
Fuel
Vj
Pj
THRUST EQUATION

## Slide 32: ENGINE PERFORMANCE PARAMETERS
Thrust/ Wt ratio
It is the ratio of sp thrust to engine wt per unit mass flow
Engine wt/ unit mass flow is related to the efficiency of engine structure and the sp. Thrust is related to the engine thermodynamics

## Slide 33: TEMPERATURE EFFECTS
GAS TURBINE ENGINES ARE VERY SENSITIVE TO VARIATION IN TEMPERATURE.
GENERALLY, THE GAS TURBINE ENGINES ARE RATED AT A STANDARD TEMP OF 15 DEG.
AS AMBIENT TEMPERATURE INCREASES, THRUST REDUCES AND THRUST INCREASES WITH DROP IN TEMPERATURE.

## Slide 36: PROP. EFFICIENCY OF DIFFERENT GAS TURBINE ENGINES

## Slide 38: TURBO PROP ENGINE

## Slide 39: FIXED SHAFT TYPE POWER CONVERSION

## Slide 40: TURBOPROP ENGINES
THIS IS BASICALLY A TURBOJET ENGINE WITH AN ADDITIONAL COMPONENT CALLED PROPELLER.
THESE PROPELLERS FORCE A LARGE MASS OF AIR (MORE THAN TURBOJET) TO ACCELARATE THUS PRODUCING THRUST( VELOCITY CHANGE IS LESSER THAN TURBOJET)
CONCENTRATION IS TO ACHIEVE HIGHER MASS FLOW THAN THE HIGHER VELOCITY CHANGES. GASES ARE NOT EXPANDED IN THE NOZZLE BUT EXPANDED IN THE TURBINE.
A MAJORITY OF GAS STREAM ENERGY IS CONVERTED INTO MECHANICAL ENERGY BY THE TURBINE
ENERGY IS UTILISED FOR DRIVING THE PROPELLERS IN FRONT OF THE ENGINE IN ADDITION TO COMPRESSOR AND ACCESSORIES

## Slide 41: TURBOPROP ENGINES

## Slide 42: CHARACTERSTICS
HIGH PROPELLER EFFICIENCY AT LOW AIR SPEEDS.
REDUCES TAKE OFF ROLL
EFFICIENCY DROPS WITH INCREASING AIR SPEED
MORE COMPLICATED IN DESIGN AND HEAVIER THAN TURBOJET
LARGE FRONTAL AREA, HENCE LONGER LANDING GEARS FOR LOW WING AIRCRAFT
EFFICIENT REVERSE THRUST POSSIBLE
SUPERIOR FOR LIFTING HEAVY LOADS AT SHORT TAKE OFF WHERE HIGH SPEEDS ARE NOT REQUIRED.

## Slide 43: TURBOFAN ENGINE

## Slide 44: TURBOFAN ENGINES
Has a duct enclosed fan mounted on the front or rear. Basically thrust augmented turbojet by dividing or increasing airflow.
Driven mechanically - geared down or at same speed as that of compressor by independent turbine located at rear of compressor-drive turbine.
Based on jet principle
Fans help increase mass flow
The fan air can exit engine separately or can be ducted back to mix with primary air at the rear, or the primary and secondary air flow can be mixed internally and then exit through a common nozzle

## Slide 45: TURBOFAN

## Slide 46: TURBOFAN ENGINE

## Slide 47: CHARACTERSTICS
Increase in FPR(Fan Pressure Ratio) results in increase in fan thrust.
For any value of TIT, there is an optimum value of FPR
Optimum value of FPR for minimum SFC & max. Sp. Thrust coincide because of fixed energy input

## Slide 48: CHARACTERSTICS
Increasing BPR(By Pass ratio) improves SFC at the expense of a significant reduction in Sp. thrust
Optimum FPR increases with TIT
Optimum SFC requires low Sp thrust, this being particularly important for high bypass turbofans.

## Slide 49: Turboshaft Engine

## Slide 50: TURBOSHAFT ENGINES
Low weight, small size and large power output
Ideally suited for helicopter use
Main Parts of a Turboshaft engine
  Air inlet or Diffuser
  Gas generator compressor
  Combustion chamber
  Gas generator turbine
  Power turbine
  Exhaust nozzle

## Slide 51: CHARACTERSTICS
Turboshaft engine must produce shaft power to drive the rotor. Hence another turbine section, the power turbine is placed in engine
Power turbine is commonly provided separately. It can be additional turbine on the gas generator turbine as in case of some turboprop engines

## Slide 52: CHARACTERSTICS
More commonly there are two separate components
  The gas generator compressor and turbine on one shaft and the power turbine on a second shaft
  Both turbines are linked aerodynamically
  Power turbine speed of 20,000 to 40,000 rpm is reduced to rotor speeds of 200 to 400 rpm through reduction gear box

## Slide 53: CHARACTERSTICS
Shaft horse power (SHP) is the output measured at the engine output shaft which is driven by the power turbine.
Output shaft rpm is reduced from free turbine rpm in the order of 2 to 4. (from 24000 to 6000). This speed is further reduced to the helicopter speed through transmission reduction gearing

## Slide 54: PROPFAN ENGINES
HAS A DUCT ENCLOSED FAN MOUNTED ON THE FRONT OR REAR
DRIVEN MECHANICALLY - GEARED DOWN OR AT SAME SPEED AS THAT OF COMPRESSOR BY INDEPENDENT TURBINE LOCATED AT REAR OF COMPRESSOR-DRIVE TURBINE.
BASED ON JET PRINCIPLE
FANS HELP INCREASE MASS FLOW
THE FAN AIR CAN EXIT ENGINE SEPARATELY OR CAN BE DUCTED BACK TO MIX WITH PRIMARY AIR AT THE REAR, OR THE PRIMARY AND SECONDARY AIR FLOW CAN BE MIXED INTERNALLY AND THEN EXIT THROUGH A COMMON NOZZLE

## Slide 55
PROPFAN ENGINE

## Slide 56: RAM JET ENGINES
It is a continuous flow jet engine with no major rotating parts
These make use of the ram effect of air at high velocities(near to sonic velocities for ramjet and supersonic velocities for scramjet)
Because of special countours of intake area, kinetic energy of high velocity air stream is conveted into static pressure energy thus increasing the pressure of the air

## Slide 57: RAMJET ENGINE
Temp is raised by adding heat in the combustion chamber and then hot high pressure mass of air is expanded in the exhaust nozzle generating the thrust.
Require high initial velocity to obtain ram effect & are unsuitable for aircraft applications
Used in missiles and target vehicles

## Slide 58
RAM JET ENGINE

## Slide 59: PULSE JET ENGINE
These engines use the principle of intermittent(pulses) combustion.
Air enters through open valves at inlet in the combustion chamber where heat is added
Heat addition , increases pressure thus closing inlet valves

## Slide 60
PULSE JET ENGINE

## Slide 61: PULSE JET ENGINE
High pressure energy is expanded in exhaust nozzle, thus producing thrust
Depression created by the exausting gases allows the valve to open and the cycle is repeated
Pulse jet engines have been designed for helicopter rotor propulsion
Not suitable as an aircraft powerplant due to high fuel consumption and unable to match performance of modern gas turbine engine

## Slide 62: ROCKET ENGINES
These engines do not use surrounding medium for propulsion
The working medium which generates the propulsive force or thrust is wholly carried within the propelled body.

## Slide 63: TYPES OF CHEMICAL ROCKET ENGINES
LIQUID PROPELLANT
SOLID PROPELLANT
GASEOUS
HYBRID

## Slide 64
SOLID PROPELLLANT ENGINES

## Slide 65
LIQUID PROPELLANT ENGINES

## Slide 66
HYBRID PROPELLANT ENGINES

## Slide 67: PERFORMANCE PARAMETERS OF ROCKET ENGINES
  COMBUSTION TEMP. (T0) IS PRIMARILY DICTATED BY CHEMISTRY OF FUEL & OXIDIZER. THE MORE REACTIVE THE PROPELLANTS ARE, THE HIGHER IS T0
  SIMILARLY THE LIGHTER THE PROPELLANT, HIGHER IS SP. IMPULSE
  FOR A GIVEN FUEL/OXIDIZER COMBINATION, WE CANNOT DO MUCH OTHER THAN CHANGE THE FUEL/OXIDIZER RATIO.

## Slide 68: SOLID PROPELLLANT ENGINES
  It consists of a casing for the propellant which joins to a nozzle of identical geometry.
  The charge of propellant in a solid rocket motor is often called the grain.
  The basic components of the grain are fuel, oxidant, binder & additives to achieve burning stability & stability in storage.

## Slide 69: SOLID PROPELLLANT ENGINES
  In most cases the grain is bonded to the wall of the combustion chamber
  Thrust depends on the rate at which grain is consumed.

## Slide 70: SOLID PROPELLLANT ENGINES
  Advantages
  Simplicity i.e absence of turbo pumps, separate propellant tanks, complicated valves & pipelines produces a high mass ratio, low cost or both
  Reliability is very high due to small no. Of individual components

## Slide 71: SOLID PROPELLLANT ENGINES
  Disadvantages
    Low exhaust velocity (2700m/s)
    Device cannot be test fired and so reliability has to be established by analogy and by quality control
  Uses
    Excel as strap on boosters and as upper stages particularly for orbital insertion

## Slide 72: SOLID PROPELLLANT ENGINES
 | Space shuttle(srb) | Mps(ariane 5)
Propellant used | Ammonium perchlorate- 68 % Al powder- 16 to 18 % Polymeric binder- 14 % Additive iron oxide – 0.4 % | 

## Slide 73: LIQUID PROPELLANT ENGINES
It comprises of the combustion chamber, nozzle & propellant tanks together with the means to deliver the propellants to the combustion chamber. Use liquid fuel and oxidiser
Liquid is pressure fed or pump fed
Design is complex as it houses liquid tanks, pumps , precision valves, pipelines etc
Combustion process is controlled

## Slide 74: LIQUID PROPELLANT ENGINES
Cooling of combustion chamber and nozzle is a must due to high temp( 3000 k)
Combustion chamber comprises injectors through which propellant enter, the vaporisation , mixing and combustion zones & restriction leading to the nozzle.
Specific injector has to take into account the nature of propellants.

## Slide 75: HYBRID PROPELLANT ENGINES
Combination of solid and liquid propellants
Has advantages of both the types and used in space launch vehicles
Gaseous propellant engine
Use high pressure stored gas as their working fluid
It requires heavy tanks and complicated systems

## Slide 76
THERMAL EFFICIENCY
PROPULSIVE EFFICIENCY
ENGINE EFFICIENCY
OVERALL CYCLE EFFICIENCY
SPECIFIC FUEL CONSUMPTION
SPECIFIC THRUST

## Slide 77
Thermal efficiency indicates the thermodynamic capacity of the cycle to convert heat into work.
Propulsive efficiency is a measure of the effectiveness of the engine in propelling the aircraft or conversion capability of KE into thrust. Ratio of useful work output to energy input.
Engine efficiency is the energy conversion capacity of the powerplant i.e. conversion rate of energy supplied by fuel to KE.

## Slide 78
Overall efficiency is a product of propulsive and engine efficiency
SFC is fuel consumption per unit thrust and helps in discarding efficiency. This helps in deciding economic feasibility.
Specific Thrust is the thrust per unit mass flow of air. This helps in deciding the size, frontal area, drag, relative size of engines for same thrust etc.